Press Release

2018-602

Schmitz Cargobull AG

The Schmitz Cargobull V.KO van body - for the final stretch

June 2018 – At the IAA Commercial Vehicles Show 2018, Schmitz Cargobull will present its solution for van bodies for last mile logistics, i.e. inner-city delivery transport. With the V.KO modular kit, Schmitz Cargobull offers a quick and easy solution for van box bodies. The V.KO van box bodies also make Schmitz Cargobull an OEM partner on a European level, with quick and transparent availability of modular box bodies within 14 working days ex works.

The V.KO Dry van box body kit consists of newly developed GRP sandwich panels. These are produced at the manufacturing plant in Berlin. The panels, which have a PU foam core, are light, robust, and at the same time only 20 mm thick. The V.KO Dry is available with a translucent light roof and a two-wing rear door as standard. A reliable and safe-to-operate handle is already integrated in the rear collision guard and an access ladder can be optionally fitted into the rear module. The walls, including the high-quality aluminium corner profiles, are available for selection in various white tones. The position lights at the front and rear as well as the third braking light are integrated and protected in the profile. All electric wiring is prepared at the factory. Likewise, an LED light with a motion sensor is integrated in the basic equipment inside the cargo area.

The V.KO Dry box body kit from Schmitz Cargobull is delivered to the body builder or OEM as a complete kit for assembly. The walls are prefabricated – along with all fittings and profiles. The sophisticated and intelligent component joining technology makes for quick and easy assembly of the box body. A special industrial adhesive makes it easy to adjust and move the sub-modules into the correct position during construction. The consoles, pre-mounted on l-beams at the factory, have already been prefabricated for the requisite chassis.

The certified body strength in accordance with DIN EN 12642, the service life / strength test with an acceleration of up to 4g or climate/temperature tests provide proof of the durability of the V.KO Dry box body set.

Access to the very well-developed Schmitz Cargobull European service network (1,700 service partners) ensures a quick response in the event of repairs. The Schmitz Cargobull service network guarantees Europe-wide availability of original spare parts, complete spare part documentation and a complete after-sales programme.

2018-602

About Schmitz Cargobull

With an annual production of some 61,000* trailers and around 6,400* employees, Schmitz Cargobull AG is Europe's leading manufacturer of semi-trailers, trailers and truck bodies for temperature-controlled freight, general cargo and bulk goods. The company achieved sales of more than € 2.2* billion in the 2017/2018 financial year. As a pioneer in the industry, the North German company developed a comprehensive brand strategy early on and consistently established quality standards spanning every level: from research and development, to production and specialist services such as consulting, trailer telematics, financing, spare parts and used vehicles.

*Provisional figures for the 2017/2018 financial year. The figures for the past financial year (01/04/2017 – 31/03/2018) will be published by the Group in September 2018.

The Schmitz Cargobull press team:

Anna Stuhlmeier	+49 2558 81-1340 I anna.stuhlmeier@cargobull.com

Andrea Beckonert	+49 2558 81-1321 I andrea.beckonert@cargobull.com
Silke Hesener:	+49 2558 81-1501 I silke.hesener@cargobull.com